## Slide 1
2025 Edge Computing Machine Learning, EE – EE 590
Spring 2025
Real‑Time Walking Speed Estimation & Gait Analysis
Using Ultrasonic sensor and Edge AI
Department of Electrical & Computer Engineering
School of Engineering, UAB
Charith Sai Sathvik Ale
S. Abdollah Mirbozorgi

## Slide 2: Overview
Motivation & Problem Statement
Comparison & Required Features
Proposed System Concept
System Architecture
Experimental Setup
Data Log
NN Model Validation
Results: Speed Estimation
Conclusion & Future Work
Acknowledgements & References

## Slide 3: Motivation
Early marker of motor decline: slow walking speed.
Falls, cognitive decline, neurodegenerative risk can be predicted by gait changes.
Need continuous, wearable, low‑cost monitoring in real world.

## Slide 4: Problem Statement
Existing lab solutions (optical capture, mats, IMUs) are expensive, bulky, lab‑bound. ​
Wearables often uncomfortable, require frequent calibration
Goal: build a low cost wearable that estimates walking speed (0.5–1.5 m/s) and hip/inter‑leg angle, entirely on‑device, real‑time, with LoRa telemetry
Must work outside controlled labs, with minimal calibration.

## Slide 5: Comparison & Required Features
Approach | Pros | Cons | Required for Our System
Video‑based motion capture | High accuracy | Expensive, fixed setup | ❌
Wearable IMUs | Portable | Calibration, comfort trade‑offs | Partial
Pressure mats | Accurate gait metrics | Floor‑embedded, non‑portable | ❌
Ultrasonic + Edge AI | Low cost, real‑time, wearable | Needs robust signal processing | ✅
​ |  |  | 

## Slide 6: Proposed Concept
Sensor: HC‑SR04 ultrasonic module mounted at knee
Edge Device: ESP32 running lightweight ML & LoRa stack
Data Flow:
Ultrasonic Sensor
Lora 32 Module

## Slide 7: System Architecture & Algorithm
Block Diagram:
Algorithm Highlights:
50 Hz loop via micros() timing
Peak detection toggles rising flag on φ vs. φPrev
Rolling average over BUF_SIZE=5 for step length
Data output: phiMax, dtStep, avgStepLen, avgStrideLen, Speed

## Slide 8: Experimental Setup
Subject: Volunteer walks 7.0 m corridor at varied speeds
Sensor placement: 0.1 m lateral offset from knee pivot
Data logging: Serial CSV captured via IDE Cool Term and saved

## Slide 9: Data Log
The serial plotter showing the raw data capturing step frequency on y- axis with respect to time.

## Slide 10: NN Model Validation
Test Accuracy: 0.96

## Slide 11: Results
Speed Estimation:
Raw data: ±0.2 m/s spikes at large φₘₐₓ.
Time‐series plot: smooth 0.5–1.5 m/s profile.
Achieved walking speeds from ~0.3 to 1.8 m/s, matching expected range.

## Slide 12: Discussion & Validation
Meets report goals:
Real‑time,
Wearable,
Low‑cost,
Fully on-device, accurate.
​
Limitations: Mounting stability, Per‑user calibration. Tested on a single volunteer walking in a straight corridor. Needs more data across:
Diverse users (age, leg geometry, gait patterns)
Varied real‑world terrains (uneven ground, stairs, turns)
Longer recording sessions (fatigue, day‑to‑day variability)
Mitigations: Moving average.

## Slide 13: Future Work & Impact
Multi‑sensor fusion (hip + knee) for robustness.
Clinical trials on elderly/Parkinson’s cohorts.
Battery & ergonomic enclosure design.
Deployment in smart‑city and tele‑health systems.
The network achieves a 95% test accuracy on our single-subject dataset, with the majority of errors coming at the "Normal"/"Fast" boundary. This proves that, on an edge device, even a rudimentary two-feature, two-layer MLP can reliably differentiate across wide walking-speed categories in real-time.

## Slide 14: Acknowledgements & References
S. Abdollah Mirbozorgi
ChatGPT
Prasanth, H., Caban, M., Keller, U., Courtine, G., Ijspeert, A., Vallery, H., & von Zitzewitz, J. (2021). Wearable Sensor-Based Real-Time Gait Detection: A Systematic Review. Sensors, 21(8), 2727. https://doi.org/10.3390/s21082727J. Breckling, Ed., The Analysis of Directional Time Series: Applications to Wind Speed and Direction, ser. Lecture Notes in Statistics. Berlin, Germany: Springer, 1989, vol. 61.
Ugbolue, U. C., Papi, E., Kaliarntas, K. T., Kerr, A., Earl, L., Pomeroy, V. M., & Rowe, P. J. (2013). The evaluation of an inexpensive, 2D, video-based gait assessment system for clinical use. Gait & posture, 38(3), 483-489.
Zsolt Knoll, László Kocsis, Rita Kiss,Ultrasound-based measurement method for gait analysis using treadmill,IFAC Proceedings Volumes,Volume 36, Issue 15,2003,Pages 347-352,ISSN 1474-6670,https://doi.org/10.1016/S1474-6670(17)33527-9.
(https://www.sciencedirect.com/science/article/pii/S1474667017335279)M. Wegmuller, J. P. von der Weid, P. Oberson, and N. Gisin, “High resolution fiber distributed measurements with coherent OFDR,” in Proc. ECOC’00, 2000, paper 11.3.4, p. 109.

## Slide 15: References
Liu, Y., An, H., Ma, H., & Wei, Q. (2023). Online Walking Speed Estimation Based on Gait Phase and Kinematic Model for Intelligent Lower-Limb Prosthesis. Applied Sciences, 13(3), 1893. https://doi.org/10.3390/app13031893
Paramasivam, A., Jenath, M., Sivakumaran, T. S., Sankaran, S., Pittu, P. S. K. R., & Vijayalakshmi, S. (2024). Development of artificial intelligence edge computing based wearable device for fall detection and prevention of elderly people. Heliyon, 10(8).
Bauer, E. K., Bultmann, S., & Behnke, S. (2024). Marker-free human gait analysis using a smart edge sensor system. arXiv preprint arXiv:2411.09538. https://doi.org/10.48550/arXiv.2411.09538 (2007) The IEEE website. [Online]. Available: http://www.ieee.org/
Enhancing Intelligent Shoes with Gait Analysis: A Review on the Integration of Inertial Measurement Units. Sensors, 2024. https://www.mdpi.com/1424-8220/24/24/7880​ FLEXChip Signal Processor (MC68175/D), Motorola, 1996.
Bucinskas V, Dzedzickis A, Rozene J, Subaciute-Zemaitiene J, Satkauskas I, Uvarovas V, Bobina R, Morkvenaite-Vilkonciene I. Wearable Feet Pressure Sensor for Human Gait and Falling Diagnosis. Sensors (Basel). 2021 Aug 3;21(15):5240. doi: 10.3390/s21155240. PMID: 34372477; PMCID: PMC8347941.
Saha SS, Sandha SS, Srivastava M. Machine Learning for Microcontroller-Class Hardware: A Review. IEEE Sens J. 2022 Nov 15;22(22):21362-21390. doi: 10.1109/jsen.2022.3210773. Epub 2022 Oct 5. PMID: 36439060; PMCID: PMC9683383.